## Slide 1
Design and Analysis of Class EF2 Inverter
Under the supervision of :
Prof. Rajeev Kumar Singh
Department of Electrical Engineering
Presented By:
Ankit Singh(23084003)

## Slide 2
Outline of Presentation
  Introduction
  CLASS EF2 INVERTER: OVERVIEW
  CIRCUIT COMPONENTS AND OPERATION
  MATHEMATICAL ANALYSIS AND DESIGN EQUATIONS
  SIMULATION RESULTS
  Conclusion

## Slide 3
Introduction
  The increasing demand for energy-efficient power electron ics has driven research into high-frequency inverter topologies for applications such as wireless power transfer (WPT), radio frequency (RF) systems, and resonant DC–DC converters.
  These applications require inverters that can operate at high frequencies with low switching losses, reduced component stress, and high efficiency.
  Conventional inverter topologies such as Class D, Class E, and Class F are widely used. Class D suffers from high switching losses due to hard switching. Class E enables zero voltage switching (ZVS) but experiences high peak voltage stress.

## Slide 4
  Class F reduces switching losses using harmonic tuning but increases design complexity.
  To address these challenges, the Class EF2 inverter incor porates a second-harmonic resonant network into the Class E structure, achieving improved efficiency and reduced device stress
Introduction

## Slide 5
CLASS EF2 INVERTER: OVERVIEW
  Combines features of Class E and Class F
  Maintains Zero Voltage Switching (ZVS)
  Uses second-harmonic tuning
  Shapes drain voltage waveform
  Reduces peak switch voltage
  Peak voltage reduced to ~2–3 Vdd
  Lower than Class E (~3.56 Vdd

## Slide 6
Circuit Diagram of Class EF2 Inverter

## Slide 7
CIRCUIT COMPONENTS AND OPERATION
  DC Supply and Feed Inductor (Lchoke):
A large RF choke connects the DC supply VDD to the drain. It provides high impedance at switching frequency, ensuring nearly constant current
  Switching Device:
A MOSFET or GaN HEMT operates as a switch driven at frequency f0 with duty cycle D ≈ 0.4–0.5.
3.Shunt Capacitance (Cs):
This includes intrinsic capacitance Coss and shapes the voltage waveform, enabling ZVS

## Slide 8
CIRCUIT COMPONENTS AND OPERATION
  Second Harmonic Tank (L2 −C2):
This parallel resonant circuit is tuned to 2f0 and blocks second harmonic current, modifying the voltage waveform.
5. Load Network (Lr −Cr −RL):
A series resonant network tuned to f0 ensures sinusoidal current delivery to the load.

## Slide 9
OPERATION OF CLASS EF2 INVERTER
On-State (0 ≤ ωt < 2πD)
The transistor conducts and vDS ≈ 0. Current flows through the switch.
Off-State(2πD≤ωt<2π) The switch is off,and the choke current charges the capacitance.The drain voltage rises and returns smoothly to zero.

## Slide 10
ROLE OF SECOND HARMONIC TANK
The second-harmonic tank is tuned to:
f0=2f0
It confines second harmonic current and shapes the drain voltage waveform, reducing peak voltage. This reduces voltage stress from3.56VDD (Class E) to approximately2–3VDD.

## Slide 11
MATHEMATICAL ANALYSIS AND DESIGN EQUATIONS

## Slide 12
1) The switching device operates as an ideal switch with zero on-resistance and infinite off-resistance.
2) The DC feed inductance L choke is sufficiently large so that the supply current Iin remains constant over a switching cycle.
3) The series load network(Lr–Cr–RL) has a high quality factor, ensuring sinusoidal output current at the fundamental frequency.
4) The shunt capacitance Cs is linear and constant, representing the transistor output capacitance.
5) All passive components are assumed lossless.
Assumption

## Slide 14
PSIM-based simulation model of the designed Class EF2 inverter using calculated component values

## Slide 15
deatils of Elements used in simulation

## Slide 16
SIMULATION RESULTS

## Slide 17
Output Waveform of Vsw and Isw

## Slide 18
Output Voltage Waveform across the load

## Slide 19
INVERTER POWER PROCESSING AND DC OUTPUT

## Slide 20
DC VOLTAGE OUTPUT

## Slide 21
Conclusion
  In this work, a Class EF2 inverter was successfully de signed, analyzed, and simulated.
  The mathematical modeling provided a clear understanding of the operating principles and enabled accurate determination of component values.
  The simulation results verified the theoretical analysis, demonstrating proper inverter operation and desired waveform characteristics.
  The addition of a transformer and rectifier stage further validated the practical applicability of the system by producing a steady DC output across the load. Overall, the Class EF2 inverter offers improved performance in terms of efficiency and reduced switching stress, making it a suitable choice for high-frequency power conversion applications

## Slide 22
Thank You!!